## Slide 1: Devices based on Quantum Tunneling
Shri Vidhatri M M
2019113006

## Slide 2: Introduction
P-N diode, BJT, MOS, CMOS : Classic semiconductor devices
Classic devices - quantum leakage currents
Electron wave behaviour and quantum tunneling paved way for new type of devices - small geometry
Tunnel diodes, Metal-insulator-metal diodes(MIM), Resonant tunnel diodes, Quantum transistors, Single electron transistors etc.
Important and most used - Tunnel diodes and MIM diodes

## Slide 3: Literature survey
Tunneling -
  Predicted by Oskar Klein
  first discovered in radioactivity
  Friedrich Hund and Leonid Mandelstam & Mikhail Leontovich independently studied
  Max Born extended tunneling beyond nuclear physics
Leo Esaki identified tunneling in semiconductors
First MIM diodes - Bell labs
Zero-bias MIM diode - Brinkman

## Slide 4: Quantum Mechanical Tunneling
Electron existing beyond classical reflection point or the penetrating a narrow barrier with V > Eele and solving the schrodinger equation for a simple case proves this.
The barrier should be thin, and of low potential energy for tunneling to happen as the tunneling probability decreases exponentially with width.
The concept is used to explain radioactive decay, field emission, current flow in p-n diode with small junction width.

## Slide 5: Tunnel diode
Heavily doped p-n diode and exhibits negative resistance.
Used in fast switching, amplifiers and high frequency devices
Advantages : resistant to heat & radiation, high speed, low cost, more stability, 2-terminal negative resistance.
A small bias voltage increases current, and even more bias voltage the current decreases, exhibiting negative resistance, on further voltage increase, behaves like regular p-n diode.
With reverse bias, current decreases faster than typical p-n diode with increasing voltage in negative direction

## Slide 6: MIM diode
Metal-insulator-metal diode : non-linear device, thin contact-film and insulator.
Has large current densities and asymmetry in I-V characteristics.
Can be used with multiple insulator layers, tunneling efficiency decreases exponentially with insulator thickness.
Some examples of metal-n insulator-metal devices are Ni/NiO/Cr, Al/AlOx/Gr, Cr/TiO2/Al2O3/Ti .

## Slide 7: Other devices
Deltt or double-electron-layer-tunneling-transistor is a device with 2 quantum wells and a thick, where tunneling is controlled by voltage bias and applied voltage in control gate
Resonant tunnel diode has two heavily doped potential barriers with small bandgap separated by a quantum well. It is very similar to tunnel diode, and has a negative differential resistance.
Single electron quantum dot transistor has a tunnel barrier enclosing the quantum dot , where the charge on dot modulates electron flow and gate voltage determines drain current in a negative resistance fashion.

## Slide 8: Conclusion
When lengths are comparable to electron wavelength, quantum effects play an important role, especially tunneling.
Devices based on Quantum tunneling work generally with high doping, involve materials of higher atomic number.
The devices where tunneling effects are prominent have I-V graphs notably different from general diodes/transistors, and most of them follow a negative resistance trend.
We observe accuracy in high frequency applications and efficiency reducing exponentially with width of layers commonly in these devices.